# Memory and Setup Clearing Procedures

# For Yokogawa’s DL750 ScopeCorder

To clear all instrument settings and the acquisition memory:

(e.g., time/div, voltage/div, cursors, markers, measurements, math, …)

- Press the SETUP button on the front of the instrument

- Press Initialize (menu key #6 on the right-hand side of the instrument’s screen) – wait for internal clicking sounds to stop and for the display to update.

- Confirm that Acquisition (ACQ) backup batteries are not installed. [The compartment for the ACQ backup batteries (4 x AA) is located on the top of the instrument on the right-hand side, next to the air vent inlet. Removing a single screw located underneath where the handle rests, opens the battery compartment.]

- If the ACQ backup batteries are installed in the compartment, either remove the batteries, or make sure that the ACQ Memory Backup switch on the right-hand size of the instrument is turned off.

- Turn off the instrument. (Power switch is located on the left-hand side of the instrument)

When the instrument is turned on again, all previous settings and any previously acquired data in acquisition memory cannot be retrieved.

To format the hard disk drive (HDD) and remove all data:

(These steps are only necessary if the DL750 has been installed with the internal hard drive option. (The internal hard disk drive is option ‘/C8’. The DL750’s model/serial number label located on the left-hand side of the instrument, below the power cord connection, will indicate whether or not the /C8 option is installed on the unit)

- Press the FILE button on the front of the instrument

- Select ‘Utility’ (menu key #7 on right-hand side of the instrument’s screen). On the screen you will now see the ‘File List’ window.

- Using the blue scroll knob on the front of the instrument, highlight ‘HD-0’ on the ‘File List’ menu. Once it is highlighted, press the SELECT button on the front of the instrument. Confirm that ‘PATH = HD-0’ is display on the ‘File List’ menu

- Select ‘Function’ (menu key #1) and then select ‘Format’ (menu key #5)

- Select ‘Format’ (menu key #4) and then select ‘Exec’ (menu key #7). Use the blue scroll knob to highlight ‘OK’ on the Confirm menu.

- Press ‘Exec’ (menu key #7) to format the HDD

After formatting the HDD, all previously stored data cannot be retrieved.